## Slide 1: VLSI Design ECE 09.414 CMOS VLSI Design
Adam Fifth
Henry M. Rowan College of Engineering
Department of ECE
Rowan University

## Slide 2: Lecture 2: CMOS Transistor Theory

## Slide 3: Outline
Introduction
MOS Capacitor
nMOS I-V Characteristics
pMOS I-V Characteristics
Gate and Diffusion Capacitance

## Slide 4: Introduction
So far, we have treated transistors as ideal switches
An ON transistor passes a finite amount of current
  Depends on terminal voltages
  Derive current-voltage (I-V) relationships
Transistor gate, source, drain all have capacitance
  I = C (DV/Dt) -> Dt = (C/I) DV
  Capacitance and current determine speed

## Slide 5: MOS Capacitor
Gate and body form MOS capacitor
Operating modes
  Accumulation
  Depletion
  Inversion
Notes: Lecture 4:

## Slide 6: Terminal Voltages
Mode of operation depends on Vg, Vd, Vs
  Vgs = Vg – Vs
  Vgd = Vg – Vd
  Vds = Vd – Vs = Vgs - Vgd
Source and drain are symmetric diffusion terminals
  By convention, source is terminal at lower voltage
  Hence Vds  0
nMOS body is grounded. First assume source is 0 too.
Three regions of operation
  Cutoff
  Linear
  Saturation

## Slide 7: nMOS Cutoff
No channel
Ids ≈ 0

## Slide 8: nMOS Linear
Channel forms
Current flows from d to s
  e- from s to d
Ids increases with Vds
Similar to linear resistor

## Slide 9: nMOS Saturation
Channel pinches off
Ids independent of Vds
We say current saturates
Similar to current source

## Slide 10: I-V Characteristics
In Linear region, Ids depends on
  How much charge is in the channel?
  How fast is the charge moving?

## Slide 11: Channel Charge
MOS structure looks like parallel plate capacitor while operating in inversions
  Gate – oxide – channel
Qchannel = CV
C = Cg = eoxWL/tox = CoxWL
V = Vgc – Vt = (Vgs – Vds/2) – Vt
Cox = eox / tox

## Slide 12: Long Channel I-V
What’s missing?
Vt?
Nothing happens b/w Vgs and Vt so we always subtract Vt

## Slide 13: Carrier velocity
Charge is carried by e-
Electrons are propelled by the lateral electric field between source and drain
  E = Vds/L
Carrier velocity v proportional to lateral E-field
  v = mE m called mobility
Time for carrier to cross channel:
  t = L / v
Notes: CH 2 pg 66

## Slide 14: nMOS Linear I-V
Now we know
  How much charge Qchannel is in the channel
  How much time t each carrier takes to cross

## Slide 15: nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
  When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current

## Slide 16: nMOS I-V Summary
Shockley 1st order transistor models

## Slide 17: Example
We will be using a 0.6 mm process for your project
  From AMI Semiconductor
  tox = 100 Å
  m = 350 cm2/V*s
  Vt = 0.7 V
Plot Ids vs. Vds
  Vgs = 0, 1, 2, 3, 4, 5
  Use W/L = 4/2 l

## Slide 18: pMOS I-V
All dopings and voltages are inverted for pMOS
  Source is the more positive terminal
Mobility mp is determined by holes
  Typically 2-3x lower than that of electrons mn
  120 cm2/V•s in AMI 0.6 mm process
Thus pMOS must be wider to
provide same current
  In this class, assume
  mn / mp = 2

## Slide 19: Capacitance
Any two conductors separated by an insulator have capacitance
Gate to channel capacitor is very important
  Creates channel charge necessary for operation
Source and drain have capacitance to body
  Across reverse-biased diodes
  Called diffusion capacitance because it is associated with source/drain diffusion

## Slide 20: Gate Capacitance
Approximate channel as connected to source
Cgs = eoxWL/tox = CoxWL = CpermicronW
Cpermicron is typically about 2 fF/mm
Notes: “Chapter 2: Long channel I-V characteristics” in book

## Slide 21: Diffusion Capacitance
Csb, Cdb
Undesirable, called parasitic capacitance
Capacitance depends on area and perimeter
  Use small diffusion nodes
  Comparable to Cg
  for contacted diff
  ½ Cg for uncontacted
  Varies with process